## Slide 1
TECHNOLOGICAL CHINA
Sergio Gevatschnaider · Sergio Gevatschnaider
01
From models
to agents and robots
Technological China · Class 2 · Intelligent systems and production.
Sergio Gevatschnaider
Instituto Confucio UBA · October 27, 2026
CONCEPTUAL ILLUSTRATION
Notes: Core material.
Connect to class 1: China combines industry, research and coordination. Today focuses on systems that perform tasks. The supplied cover is a conceptual illustration, not an identified industrial deployment.
Sources and scope:
Sergio Gevatschnaider · AI and Robotics in China
https://github.com/sgevatschnaider/Inteligencia-Artificial-y-Rob-tica-en-China

## Slide 2
TECHNOLOGICAL CHINA
The class connects technical capability to outcomes
A 60-minute core route with extensions for later study.
Sergio Gevatschnaider
02
01
Foundations · 8 min
Agent, environment and tool use.
02
Models and platforms · 12 min
DeepSeek, Qwen and distribution.
03
Robotics and videos · 17 min
Physical architecture and observable evidence.
04
Lab · 15 min
Energy, operational success and cost.
05
Discussion · 8 min
Competitiveness, work and opportunities.
Notes: Core material.
The kit contains more material than one class. Follow the teaching guide and leave extension slides for reference. Each video should answer a specific question.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 3
TECHNOLOGICAL CHINA
Economic value appears in correct, repeatable tasks
A model capability needs integration and operating conditions.
Sergio Gevatschnaider
03
Capability
Solve a task under defined conditions.
Reliability
Repeat it with measured errors and limits.
Economics
Create net value after integration and operation.
Notes: Core material.
A model that classifies invoices accurately still needs accounting integration and exception handling. Robotics adds calibration, safety and support. Distinguish technical success from realized savings.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 4
TECHNOLOGICAL CHINA
Model, chatbot, agent and robot describe different functions
They can be combined within one product.
Sergio Gevatschnaider · Russell & Norvig
04
Model
Component that predicts or generates outputs.
Chatbot
Conversational interface with a user.
Agent
System that observes, decides and acts.
Robot
Machine that senses and acts physically.
Notes: Core material.
An industrial robot may operate without an LLM and a chatbot may use tools. These are functions and architectures rather than an intelligence hierarchy.
Sources and scope:
Russell & Norvig · Artificial Intelligence: A Modern Approach
https://aima.cs.berkeley.edu/

## Slide 5
TECHNOLOGICAL CHINA
Five layers connect research to production
A company’s advantage also depends on suppliers and channels.
Sergio Gevatschnaider · Sergio Gevatschnaider
05
01
Models
DeepSeek, Qwen and other families.
02
Agent systems
Orchestration, tools and evaluation.
03
Cloud and distribution
Access to compute, users and services.
04
Infrastructure
Chips, memory, interconnects and energy.
05
Physical world
Factories, sensors, robots and support.
Notes: Core material.
The layers are not a one-way chain: usage data and constraints feed back into design. Companies may compete in models while cooperating on infrastructure. This is a functional map, not a ranking.
Sources and scope:
Sergio Gevatschnaider · AI and Robotics in China
https://github.com/sgevatschnaider/Inteligencia-Artificial-y-Rob-tica-en-China

## Slide 6
TECHNOLOGICAL CHINA
Strategies combine models, platforms and infrastructure
These examples illustrate different ecosystem positions.
Sergio Gevatschnaider · Sergio Gevatschnaider / Qwen-Agent / DeepSeek-V3
06
DeepSeek
Research on models and compute efficiency.
Alibaba / Qwen
Models and tools connected to cloud and distribution.
Huawei
Sector models and computing infrastructure.
Notes: Extension material.
These are neither exclusive categories nor claims of self-sufficiency. Infrastructure, community and distribution can be strategic complements. Specific integrations need product-level verification.
Sources and scope:
Sergio Gevatschnaider · AI and Robotics in China
https://github.com/sgevatschnaider/Inteligencia-Artificial-y-Rob-tica-en-China
Qwen-Agent · official code and documentation
https://github.com/QwenLM/Qwen-Agent
DeepSeek-V3 · technical report, Table 1 (2024–2025)
https://arxiv.org/abs/2412.19437

## Slide 7
TECHNOLOGICAL CHINA
DeepSeek-V3 activates a fraction of its parameters per token
MoE routes processing through selected experts.
Sergio Gevatschnaider · DeepSeek-V3
07
MoE
671 billion
Total parameters of V3 in the report.
37 billion
Parameters activated per token, according to the report.
Implication
Less activation does not remove memory, communication or complexity.
Notes: Extension material.
This is a dated case study, not a description of the newest version. Total parameters do not equal work per token. Routing and accelerator communication matter for system performance.
Sources and scope:
DeepSeek-V3 · technical report, Table 1 (2024–2025)
https://arxiv.org/abs/2412.19437

## Slide 8
TECHNOLOGICAL CHINA
R1 and R1-Zero use different training paths
Both start from a pretrained base.
Sergio Gevatschnaider · DeepSeek-R1
08
Pretrained base
Capabilities acquired from large corpora.
R1-Zero
Reinforcement learning without preliminary SFT in that experiment.
R1
Cold-start data, reinforcement stages and additional tuning.
Notes: Core material.
R1-Zero does not mean training from scratch. Distinguish the reinforcement experiment from the fuller R1 pipeline. The paper reports its own results, and a reasoning model is not a complete agent system.
Sources and scope:
DeepSeek-R1 · technical report (2025)
https://arxiv.org/abs/2501.12948

## Slide 9
TECHNOLOGICAL CHINA
The reported V3 cost has a specific scope
The figure covers official training compute under an assumed rental price.
Sergio Gevatschnaider · DeepSeek-V3
09
US$5.576m
What it calculates
2.788 million H800 hours × US$2 per hour.
What it excludes
Prior research and ablation experiments.
What it does not measure
Total company costs or the full development of R1.
Notes: Core material.
Table 1 includes reported V3 pretraining, context extension and post-training. It uses an assumed rental price, not audited accounts. Distinguish training, inference, research and commercial pricing.
Sources and scope:
DeepSeek-V3 · technical report, Table 1 (2024–2025)
https://arxiv.org/abs/2412.19437

## Slide 10
TECHNOLOGICAL CHINA
Model selection requires a task-level evaluation
A general benchmark does not replace a use-case test.
Sergio Gevatschnaider
10
Quality
Success on representative data and difficult cases.
Latency and cost
Total time, tokens, tools and retries.
Access and license
Weights, API and terms for the chosen variant.
Operations
Privacy, language, availability and support.
Notes: Extension material.
Open weights, open-source code and APIs are different access modes. Variants may have different licenses. Compare models on the same tasks with dated configuration and budget.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 11
TECHNOLOGICAL CHINA
Qwen and Qwen-Agent occupy different levels
System capability depends on configured components.
Sergio Gevatschnaider · Qwen-Agent
11
Qwen
Model family with variants and modalities.
Qwen-Agent
Framework for integrating models and tools.
Application
A product’s interface, permissions, data and services.
Notes: Core material.
Qwen-Agent documents tool use and retrieval. An arbitrary installation does not automatically gain payments or commerce access. Commercial integrations have specific scope, regions and conditions.
Sources and scope:
Qwen-Agent · official code and documentation
https://github.com/QwenLM/Qwen-Agent

## Slide 12
TECHNOLOGICAL CHINA
Distribution can turn capability into adoption
A channel reduces friction when it solves an existing user need.
Sergio Gevatschnaider
12
Access
Existing users and service discovery.
Integration
Connected data, processes and tools.
Retention
Recurring quality and switching costs.
Notes: Extension material.
This is an economic interpretation, not an accounting identity or guarantee of market power. Integration may also raise dependence and exit costs. Ask whether clients can export data and reproduce the process elsewhere.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 13
TECHNOLOGICAL CHINA
Tools make parts of execution verifiable
The log should distinguish request, result and validation.
Sergio Gevatschnaider · Qwen
13
Model
Requests a function and proposes arguments.
Application
Validates scope, arguments and permissions.
Tool
Calculates, searches, opens or modifies a resource.
Verification
Checks the result before concluding.
Notes: Core material.
An editing agent needs to open the final file. A data agent needs reproducible calculations. Tools return observations and may fail. The architecture needs explicit handling of errors and missing data.
Sources and scope:
Qwen · Function Calling documentation
https://qwen.readthedocs.io/en/stable/framework/function_call.html

## Slide 14
TECHNOLOGICAL CHINA
Supplier research requires normalization before comparison
A fictional exercise on sources and comparison criteria.
Sergio Gevatschnaider
14
01
Same task
Handle the same part under the same requirements.
02
Same measure
Per-hand, total or recommended payload: define scope.
03
Same evidence
Source, date, variant and operating test.
04
Output
Table with uncertainty and testing needs.
Notes: Core material.
Use the agent simulator to introduce a unit mismatch and a missing field. The exercise does not rank suppliers. It teaches traceability and the ability to acknowledge insufficient evidence.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 15
TECHNOLOGICAL CHINA
A persuasive demo needs an evidence record
Assess what actually ran and could be checked.
Sergio Gevatschnaider
15
Claim
“I compared the three best suppliers.”
Record
Opened sources, extracted fields and operations.
Validation
Selection criteria and rejected alternatives.
Notes: Extension material.
Ask for execution evidence before judging prose. A primary source documents a declared specification but may not independently validate performance. Separate observations, declarations and analyst inference.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 16
TECHNOLOGICAL CHINA
Embodied intelligence connects perception to physical action
具身智能 · jùshēn zhìnéng.
Sergio Gevatschnaider · OpenVLA
16
具身智能
jùshēn zhìnéng
Perception
Interpret objects, contact and position.
Decision
Choose an action based on task and state.
Control
Execute motion and correct deviations.
Notes: Core material.
The term refers to intelligence operating through a body in an environment. It does not imply human understanding or that the entire architecture is an LLM. Sensorimotor coupling and test conditions are central.
Sources and scope:
OpenVLA · research paper (2024)
https://arxiv.org/abs/2406.09246

## Slide 17
TECHNOLOGICAL CHINA
Robot architecture separates goals from control
Layers address different problems and timescales.
Sergio Gevatschnaider
17
01
Task
Select the object and destination.
02
Perception and state
Estimate pose, obstacles and contact.
03
Policy and trajectory
Choose actions or motion references.
04
Control and actuators
Regulate forces and motion with feedback.
Notes: Core material.
Feedback updates control. An LLM can sit at a high level without commanding every motor. Operational protection must intervene when planning proposes an unsuitable action.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 18
TECHNOLOGICAL CHINA
A VLA conditions actions on vision and instructions
Vision–Language–Action combines modalities for a robotic task.
Sergio Gevatschnaider · OpenVLA
18
Input
Image, instruction and available state.
VLA policy
Prediction of actions or action sequences.
Execution
Conversion to motion through the control system.
Notes: Core material.
OpenVLA is a research reference for architecture, not a Chinese product or universal standard. Generalization is tested under defined tasks and conditions. End-to-end integration does not remove evaluation or safety.
Sources and scope:
OpenVLA · research paper (2024)
https://arxiv.org/abs/2406.09246

## Slide 19
TECHNOLOGICAL CHINA
Robots learn from demonstrations, interaction and simulation
Each data source brings different information and limitations.
Sergio Gevatschnaider · OpenVLA / Sutton & Barto
19
Teleoperation
A human demonstrates a task.
Imitation
A policy learns observation–action relationships.
Simulation and RL
Scenario exploration with a defined objective.
Physical tests
Validation with real contact, failures and variability.
Notes: Extension material.
Simulation and imitation can be combined. Dataset diversity and evaluation design matter alongside size. Skills learned with one gripper do not automatically transfer to a different hand.
Sources and scope:
OpenVLA · research paper (2024)
https://arxiv.org/abs/2406.09246
Sutton & Barto · Reinforcement Learning, second edition
http://incompleteideas.net/book/the-book-2nd.html

## Slide 20
TECHNOLOGICAL CHINA
Simulation leaves a gap to the real world
A simulator approximates friction, contact, sensors and dynamics.
Sergio Gevatschnaider
20
What changes
Surfaces, lighting, mass and wear.
How to narrow the gap
Scenario variation, calibration and adaptation.
What to check
Success and safety under unseen conditions.
Notes: Extension material.
More synthetic data does not always improve results. Its value depends on relevant variation and avoiding bias. Final testing must specify hardware, task and operating conditions.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 21
TECHNOLOGICAL CHINA
Industrial policy needs implementation indicators
An announced target and deployed capability require different evidence.
Sergio Gevatschnaider
21
Inputs
Funding, talent and infrastructure.
Activities
Labs, training and industrial integration.
Outcomes
Adoption, quality, productivity and safety.
Notes: Extension material.
The original deck included deployment targets without sufficiently visible dating. This version replaces them with an evaluation framework to avoid turning announcements into achievements. Future figures need document, date, scope and deadline.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 22
TECHNOLOGICAL CHINA
Unitree, UBTECH and XPENG show three starting points
The comparison identifies emphasis, not a universal winner.
Sergio Gevatschnaider · Unitree / UBTECH / XPENG
22
Unitree
Hardware, mobility and research platforms.
UBTECH
Integration of humanoids into industrial processes.
XPENG
Transfer of capabilities from vehicles and manufacturing.
Notes: Core material.
Strengths are interpretations of company positioning and need task-level evaluation. Do not rank different configurations by degrees of freedom alone. Uptime, manipulation, integration and support matter.
Sources and scope:
Unitree · G1 product specifications
https://www.unitree.com/g1/
UBTECH · Walker S2 manufacturer page
https://www.ubtrobot.com/en/humanoid/products/walker-s2
XPENG · IRON production line announcement, 08/09/2026
https://www.xpeng.com/news/01a080371029a057bc8e8a02a2c6012b

## Slide 23
TECHNOLOGICAL CHINA
G1 illustrates mobility and hardware configuration
The manufacturer’s specifications describe conditional capabilities.
Sergio Gevatschnaider · Unitree
23
G1
≈ 132 cm
Declared G1 height.
≈ 35 kg
Declared weight depending on configuration.
Operating question
How many valid tasks does it complete without intervention?
Notes: Core material.
These are manufacturer declarations, not measurements by this class. Record variant and accessories. The side-flip video shows dynamic control while leaving industrial task productivity unresolved.
Sources and scope:
Unitree · G1 product specifications
https://www.unitree.com/g1/
Unitree · G1 side flip, original video
https://www.youtube.com/watch?v=29xLWhqME2Q

## Slide 24
TECHNOLOGICAL CHINA
Walker S2 motivates a discussion of uptime
UBTECH declares autonomous battery swapping within three minutes.
Sergio Gevatschnaider · UBTECH
24
≤ 3 min
Energy
Replenishment reduces one source of downtime.
Reliability
Failures, parts, maintenance and assistance still matter.
Metric
Availability = available hours / planned hours.
Notes: Core material.
The page supports a declared capability, not continuous productive operation. Include station, batteries, maintenance and recovery time. Availability is distinct from task success.
Sources and scope:
UBTECH · Walker S2 manufacturer page
https://www.ubtrobot.com/en/humanoid/products/walker-s2

## Slide 25
TECHNOLOGICAL CHINA
IRON links automotive manufacturing to robotics
Company announcement dated September 8, 2026.
Sergio Gevatschnaider · XPENG
25
01
Reported as completed
Commissioning a line and producing a robot.
02
Declared target
Mass production targeted for late 2026.
03
Commercial plan
Launch and deliveries planned for 2027.
Notes: Core material.
Treat the announcement as XPENG’s statement. Avoid adopting promotional leadership claims. Reported milestones and future plans have different status. Deliveries, clients and operating hours are needed to assess commercialization.
Sources and scope:
XPENG · IRON production line announcement, 08/09/2026
https://www.xpeng.com/news/01a080371029a057bc8e8a02a2c6012b

## Slide 26
TECHNOLOGICAL CHINA
A useful comparison retains task, version and conditions
Missing data belongs in the comparison.
Sergio Gevatschnaider
26
Dimension | Evaluation question
Locomotion | Which surface and what stability?
Manipulation | Which object, precision and repeatability?
Autonomy | How much intervention and remote assistance?
Operations | What uptime and support?
Economics | What cost per correct task?
Notes: Extension material.
This is an evaluation template, not a completed empirical comparison. Do not fill fields using video-based guesses. Comparable testing or explicitly identified data are required.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 27
TECHNOLOGICAL CHINA
Videos have a dedicated page for observation and discussion
Each demonstration includes a question and an evidence limitation.
Sergio Gevatschnaider · VideoLab / Unitree / XPENG / UBTECH
27
G1 · dynamic control
Observe balance and motion recovery.
IRON · locomotion
Distinguish human-like appearance from autonomy.
Walker S2 · battery
Ask what is missing to assess uptime.
Notes: Core material.
Open videos.html from the portal. Show brief teacher-selected excerpts without unverified timing claims. If embedding is blocked, open the original. Links were retrieved, but audiovisual playback was not validated in this environment.
Sources and scope:
VideoLab · existing teaching catalog
https://sgevatschnaider.github.io/Inteligencia-Artificial-y-Rob-tica-en-China/videolab/
Unitree · G1 side flip, original video
https://www.youtube.com/watch?v=29xLWhqME2Q
XPENG · Why is IRON so human-like?, original video
https://www.youtube.com/watch?v=ssxdSVQN14I
UBTECH · Walker S2 manufacturer page
https://www.ubtrobot.com/en/humanoid/products/walker-s2

## Slide 28
TECHNOLOGICAL CHINA
A data flywheel requires usage to improve the system
Interaction data connect perception, action and outcome.
Sergio Gevatschnaider
28
Operate
Execute tasks with recorded context.
Measure
Capture failures, interventions and outcomes.
Curate
Filter quality and expand useful diversity.
Improve
Train, test and deploy an evaluated version.
Notes: Core material.
Improvement feeds back into operation. The cycle represents a causal hypothesis to test, not an automatic result. A fleet may generate redundant data and reinforce bias when difficult cases are missing.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 29
TECHNOLOGICAL CHINA
Data quality shapes transferable learning
More recorded hours do not necessarily mean more useful information.
Sergio Gevatschnaider
29
Coverage
Parts, lighting, shifts and exceptions.
Labeling
Distinguish attempt, success, failure and recovery.
Rights
Permitted access and use of industrial data.
Transfer
Adaptation to different hardware and environments.
Notes: Extension material.
A factory’s data advantage depends on recording, curation and reuse. Not all information transfers or can be shared. Ask which institutional and engineering capabilities complement a large fleet.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 30
TECHNOLOGICAL CHINA
Autonomy and economic evidence are separate axes
Quadrants describe evidence types, not company rankings.
Sergio Gevatschnaider
30
Profitable narrow case
Narrow task and measured costs.
Validated pilot
Autonomy and cost assessed.
Prepared demonstration
Little operating evidence.
Autonomous demo
Observed capability, open economics.
More economic
evidence
Less
Less autonomy
More autonomy
Notes: Core material.
Horizontal: observed autonomy under stated conditions. Vertical: comparative economic evidence. An automated cell can be profitable with narrow autonomy. An autonomous humanoid may lack a proven economic case.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 31
TECHNOLOGICAL CHINA
Gross throughput and valid tasks measure different things
Success rate and availability modify useful output.
Sergio Gevatschnaider
31
qᵥ = q × A × r
q · gross tasks / h
Rate during an operating hour.
A · availability
Available share of scheduled time.
r · success rate
Share of tasks completed correctly.
Notes: Core material.
Keep denominators distinct. Availability applies to scheduled time and success to operating attempts. Rework is not modeled explicitly. Parameters are user assumptions, not manufacturer estimates.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 32
TECHNOLOGICAL CHINA
RobotLab retains a simple energy model
The original equations are teaching assumptions.
Sergio Gevatschnaider · RobotLab
32
E(s) = (150 + 100s² + 80w) / (30swe)
Throughput
q = 30 × s × w tasks per operating hour.
Power
W = (150 + 100s² + 80w) / e.
Energy intensity
E = W / q Wh per attempt.
Notes: Core material.
s, w and e are dimensionless multipliers. Here w raises both throughput and power: interpret it as batch or task intensity, not a physical law for kilograms. The base battery is 1,000 Wh. These equations cannot size an actual purchase.
Sources and scope:
RobotLab · original educational model
https://sgevatschnaider.github.io/Inteligencia-Artificial-y-Rob-tica-en-China/robotlab/

## Slide 33
TECHNOLOGICAL CHINA
Minimum energy occurs at an intermediate speed
At fixed w, energy per attempt first falls and then rises.
Sergio Gevatschnaider · RobotLab
33
Chart: Energy per attempt · w = e = 1
| 0.3 | 0.45 | 0.6 | 0.75 | 0.9 | 1.05 | 1.2 | 1.35 | 1.5 | 1.65 | 1.8 | 1.95 | 2.1 | 2.25 | 2.4 | 2.55 | 2.7 | 2.85 | 3 | 3.15 | 3.3 | 3.45 | 3.6 | 3.75 | 3.9 | 4.05 | 4.2 | 4.35 | 4.5
Wh / attempt | 26.5556 | 18.537 | 14.7778 | 12.7222 | 11.5185 | 10.8016 | 10.3889 | 10.179 | 10.1111 | 10.1465 | 10.2593 | 10.4316 | 10.6508 | 10.9074 | 11.1944 | 11.5065 | 11.8395 | 12.1901 | 12.5556 | 12.9339 | 13.3232 | 13.7222 | 14.1296 | 14.5444 | 14.9658 | 15.393 | 15.8254 | 16.2625 | 16.7037
s* ≈ 1,52
Energy minimum
Efficiency e rescales the curve.
This is not a factory cost optimum.
Notes: Extension material.
Write E(s) as [(150+80w)/s + 100s]/(30we). The derivative vanishes at s*=sqrt((150+80w)/100). For w=1 it is 1.5166. e rescales the curve without shifting this minimum. Success, cost and safety may change the relevant objective.
Sources and scope:
RobotLab · original educational model
https://sgevatschnaider.github.io/Inteligencia-Artificial-y-Rob-tica-en-China/robotlab/

## Slide 34
TECHNOLOGICAL CHINA
Battery energy imposes an exact time constraint
The simulation stops energy use and task accumulation at depletion.
Sergio Gevatschnaider
34
t = B / W
Runtime
t = B / W, with B in Wh and W in watts.
State
Bₜ₊Δ = max(0, Bₜ − W × Δh).
Comparison
A larger battery changes runtime, not Wh per attempt.
Notes: Extension material.
The final time step must stop at the available energy. Counting a full hour with insufficient battery overstates output. Power is constant within a scenario; degradation and thermal variation are omitted.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 35
TECHNOLOGICAL CHINA
Energy efficiency alone does not determine useful cost
The extension adds availability, success rate and annual costs.
Sergio Gevatschnaider
35
Annual valid tasks
Qᵥ = H × A × q × r.
Energy per valid task
Eᵥ = W / (q × r), during operation.
Unit cost
Total annual cost / Qᵥ.
Notes: Core material.
The model assumes energy use only during operating hours and omits idle power. Availability changes volume and energy expense, but not operating Eᵥ. Annual fixed costs spread across fewer tasks as availability falls. This avoids double counting.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 36
TECHNOLOGICAL CHINA
Total cost includes integration and operation
Compare technologies by valid task and economic horizon.
Sergio Gevatschnaider
36
Initial investment
Equipment, installation, adaptation and engineering.
Annual fixed cost
Annualized capital, support, licenses and maintenance.
Variable cost
Energy, consumables and intervention per attempt.
Notes: Core material.
The lab uses straight-line annualization: investment minus residual divided by years. It omits discounting, taxes and financing. Unit cost is not a complete financial appraisal; residual value is not annual revenue.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 37
TECHNOLOGICAL CHINA
A fixed task can favor conventional automation
Hypothetical example with annual costs already calculated.
Sergio Gevatschnaider
37
Alternative | Annual cost | Valid tasks | Cost / task
Humanoid A | US$80,000 | 40,000 | US$2.00
Arm B | US$56,000 | 70,000 | US$0.80
Notes: Core material.
The calculations are 80,000/40,000 and 56,000/70,000. They are not company prices or results. The conclusion requires comparable task requirements. Adaptability may be valuable as task mix changes, but it needs quantification.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 38
TECHNOLOGICAL CHINA
Usage volume spreads fixed costs
Lower variable cost offsets investment only with enough activity.
Sergio Gevatschnaider
38
Q* = (Fₐ − Fᵦ) / (vᵦ − vₐ)
Alternative A
Cost = Fₐ + vₐQ.
Alternative B
Cost = Fᵦ + vᵦQ.
Crossover
Q* = (Fₐ − Fᵦ) / (vᵦ − vₐ).
Notes: Extension material.
The equation assumes linear costs and a nonzero denominator. A crossover matters only when Q* is positive and feasible for both options. Match valid tasks, quality and availability. This threshold is not an investment payback period.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 39
TECHNOLOGICAL CHINA
Automation reorganizes tasks and skills
Substitution and complementarity can occur within one occupation.
Sergio Gevatschnaider
39
Changing tasks
Transport, sorting or repetitive inspection.
Complementary tasks
Diagnostics, integration, quality and supervision.
Conditions
Training, work organization and adoption.
Notes: Core material.
Technical capability alone does not determine net employment. Demand, prices and new tasks also change. Aging may encourage automation without making it profitable everywhere. Undated demographic figures from the source were omitted.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 40
TECHNOLOGICAL CHINA
“New quality productive forces” links innovation and organization
新质生产力 · xīn zhì shēngchǎn lì.
Sergio Gevatschnaider
40
新质生产力
xīn zhì shēngchǎn lì
Technology
Research and process improvements.
Capabilities
Talent, suppliers and infrastructure.
Outcomes
Observable quality and productivity.
Notes: Extension material.
Treat this as policy vocabulary and discuss its analytical content. A policy expression is not a statistical measure. The economic connection combines innovation, human capital and organizational change.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 41
TECHNOLOGICAL CHINA
Bottlenecks appear throughout the system
A component’s efficiency depends on complementary assets.
Sergio Gevatschnaider
41
Compute
Chips, memory and interconnects.
Engineering
Actuators, precision, sensors and calibration.
Operations
Energy, maintenance and local support.
Market
Demand, integration and ability to pay.
Notes: Extension material.
Connect to class 3 on semiconductors without asserting unverified trade rules. Dependencies may involve software or services as well as hardware. Commercial system availability matters alongside specifications.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 42
TECHNOLOGICAL CHINA
Argentina can supply services that make technology usable
Opportunities to assess, not a guaranteed demand forecast.
Sergio Gevatschnaider
42
Evaluation
Comparable model and task testing.
Integration
Connections to client systems and processes.
Data
Curation, evaluation and bilingual documentation.
Economics
Total cost, scenarios and process redesign.
Notes: Extension material.
This is an applied discussion of knowledge-based services. Validate demand through clients, infrastructure access and technical capability. Do not promise a market without commercial research.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 43
TECHNOLOGICAL CHINA
Chinese vocabulary helps interpret technology discussions
Research, engineering and policy concepts.
Sergio Gevatschnaider
43
具身智能
jùshēn zhìnéng
Embodied intelligence
数据飞轮
shùjù fēilún
Data flywheel
端到端
duān dào duān
End-to-end
新质生产力
xīn zhì shēngchǎn lì
New quality productive forces
机器人红利
jīqìrén hónglì
Robotic dividend (metaphor)
Notes: Extension material.
具身智能: embodied intelligence. 数据飞轮: data flywheel. 端到端: end-to-end. 新质生产力: new quality productive forces. 机器人红利: robotic dividend, used here as an analytical metaphor rather than an official indicator.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 44
TECHNOLOGICAL CHINA
The workshop asks for a decision supported by assumptions
Compare two scenarios using the lab.
Sergio Gevatschnaider
44
01
Hypothesis
“More speed reduces cost per valid task.”
02
Experiment
Change speed and then success rate, one variable at a time.
03
Evidence
Save A and B, export CSV and explain the result.
04
Limit
State what must be measured before applying it in a factory.
Notes: Core material.
The result may reject the hypothesis. With fixed success, speed spreads fixed costs across more tasks and may offset higher energy. If success drops, the conclusion may reverse. Seek reproducible reasoning rather than one predetermined answer.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 45
TECHNOLOGICAL CHINA
The portal connects decks, lab and videos
Local study materials with external links for further reading.
Sergio Gevatschnaider
45
Presentations
Editable PPTX, PDF and a reader with notes and search.
Lab
Energy, operations and an agent workflow.
Videos
Dedicated page with access to the repository VideoLab.
Teaching guide
60-minute route, answers and extensions.
Notes: Core material.
Open the module index.html. Local use needs a modern browser and no installation. Linked videos and sources need Internet. The presentations and simulators do not call external models.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.

## Slide 46
TECHNOLOGICAL CHINA
Evidence connects models, agents and productivity
The relevant outcome is a useful, repeatable and economically justified task.
Sergio Gevatschnaider
46
01
Model
What it can produce.
02
Agent
What it can execute and verify.
03
Robot
What it can perform physically.
04
Economics
What value remains after all costs.
Notes: Core material.
Close by asking for one concrete test before investing. A good answer specifies task, alternative, sample, metrics and conditions. Connect to class 3: capability also depends on chips, energy and supply chains.
Sources and scope:
Teaching explanation and example. Hypothetical calculations and scenarios are not company measurements.